## Slide 1: ANALOG to DIGITAL CONVERTER(ADC)

## Slide 2: ADC IN LPC1768
ADC uses Successive Approximation method for analog to digital conversion

## Slide 3: ADC of LPC 1768
Commonly used range 0 to 3.3V
12-bit ADC
Maximum of 8 multiplexed analog inputs are supported
Smallest voltage that cause variation in digital output is referred as resolution of ADC and is (Vrefp-Vrefn)/2^N, Ex: 3.3/2^12 = 0.805 mV
Vanalog= (VREFP / 2^N) (Decimal Equivalent of Digital value(in binary))

## Slide 4
Internally availabale on the kit
AD0.4 P1.30 in fn 3
AD0.5 P1.31 in fn 3

## Slide 5: SFRs in ADC
ADCR : A/D control registers
ADDR0 – ADDR7 : A/D data register
ADGDR : A/D global data register
ADINTEN :A/D interrupt enable register
ADSTAT : A/D conversion status is updated

## Slide 7: ADCR

## Slide 8: ADCR initialization
If input is applied on channel 5 i.e. AD0.5, then ADCR is initialized to
LPC_ADC->ADCR = 1<< 5 | 1<<21 | 1<<24;
//21 bit is PDN, 24 is to start the conversion
If input is applied to AD0.2 and AD0.5 for burst mode of operation, then LPC_ADC->ADCR =?

## Slide 9: ADGDR
DONE bit (31st bit) is made high after the completion of conversion
A/D global register (15:4) holds the result of the most recent A/D conversion that has completed, and also includes copies of status flags that go with that conversion.
Results of conversion can be read from A/D global register or A/D channel data register.

## Slide 10: ADGDR

## Slide 11: ADGDR
while(!(LPC_ADC->ADGDR & 0X80000000)); // waiting for done bit to become high
// or while((LPC_ADC->ADGDR &1<< 31)==0);
  X = (LPC_ADC->ADGDR>>4)& 0XFFF;

## Slide 12: A/D Data Register(ADDR0 TO ADDR7)
A/D data registers hold the result of last conversion for each channel.
The completion of A/D conversion is specified by DONE bit 31st

## Slide 13: ADINTEN

## Slide 14: A/D STATUS REGISTER

## Slide 15: Basic ADC configurations and accessing the digital value p1.31 as AD0.5
int main()
{ SystemInit();
SystemCoreClockUpdate ();
LPC_SC->PCONP= 1<<12;//To enable ADC
LPC_SC->PCONP |= (1<<15); //Power for GPIO block
LPC_PINCON->PINSEL3 = 3<<30; //0XC0000000
    LPC_ADC->ADCR = (1<<5)|(1<<21)|(1<<24);//AD0.5, start conversion and operational
    While(1)
    {
    while(LPC_ADC->ADGDR &1<< 31)==0); //wait till 'done' bit is 1, indicates conversion complete
    adc_temp = LPC_ADC->ADGDR;
    adc_temp >>= 4;
    adc_temp &= 0x00000FFF; //12 bit ADC
    in_vtg = (((float)adc_temp * (float)Ref_Vtg))/((float)Full_Scale);
    //calculating input analog voltage
    sprintf(vtg,"%3.2fV",in_vtg); //convert the readings into string to display on LCD, defined in stdio.h
    sprintf(dval,"%x",adc_temp); //digital equivalent
    //code to display on LCD
    }
    }

## Slide 16: Display the analog input voltage and its digital equivalent

## Slide 19: ADC with interrupts
SFRs:
  ADINTEN : To enable the interrupts

## Slide 20: AD0INTEN CONTD..

## Slide 21: Find the difference between the digital value AD0.4 and AD0.5
int main()
{
SystemInit();
SystemCoreClockUpdate();
LPC_PINCON->PINSEL3 = 0xF0000000; //p1.30 as AD0.4
LPC_SC_PCONP | =1<<12;
LPC_ADC->ADCR = 1<<4 | 1<<5 | 1<<16 |1<<21;
LPC_ADC_ADINTEN = 1<<4 | 1<<5;
NVIC_EnableIRQ(ADC_IRQn);
while(1);
}

## Slide 22: Find the difference between the digital value AD0.4 and AD0.5 contd..
Void ADC_IRQHandler()
{ int x;
int channel, temp1, temp2;
X = LPC_ADC->ADSTAT;
X=X & 3<<4;
if (X ==1<<4)
{
temp1 = LPC_ADC->ADDR4>>4;
}
elseif (X ==1<<5)
{ temp2 = LPC_ADC->ADDR5>>4;
}
//COMPLETE THE CODE TO DISPLAY THE DIFFERENCE ON MULTIPLEXED SEGMENTS
}